LED UTILITY OR UNDERCARRIAGE LIGHT

HiViz LEDs FireTech model FT-CU-P500 light shall be provided.  The light shall consist of 32  0.2W SMD LEDs.  No optics shall be placed in front of the LEDs as this fixture shall be designed primarily as a flood light.  Total power consumption shall be less than 500mA @ 12v with an operating range of 9-32V DC.  The manufacturer shall offer this product with a Limited Lifetime Warranty.

Specs:

1. OPERATING VOLTAGE : 9V - 32V DC

2. WATTAGE : 12V / 493mA / 6.0W

24V / 263mA / 6.3W

3. LED: 0.2W (SEOUL SEMICONDUCTOR)

4. LUMINOUS FLUX : 500LM

5. LENS: ACRYLIC

6. WEIGHT: 186G / 0.41 LBS

7. VIBRATION : 8.6Grms

8. WEATHER AND DUST RESISTANCE

9. TEMPERATURE : -40C - +50C

10: L70 LIFE : 50,000HR

11. IP RATNIG: IP67